Analog to Digital Conversion with Computerboards CIO-DAS1400
                            using the Linux OS
                                 Jim Bean


The CIO-DAS1400 is an a/d-converter board with 8 differential or
    16 single ended analog inputs.

This driver is an adaptation of the pacer driver for the DIO1600 board
    written by Sam Moore, Warren Jasper, Ricky Beam, Rob Cox and Jorg Weule.
The software trigger code is borrowed from the DAS1200 (Keithley) driver
    written by M Welsh.

A library is added to encapsulate the lower level functions.
Because my application is in Ada, an Ada interface and test program is included.

With this driver you can operate in several modes:

   Data aquisition without pacer: Conversion is done from time to time
     on specified channels under control of either the application program
     or an external trigger source.

   Data aqusition with pacer: The channels are sampled with a constant
     hardware supplied sampling frequency.

Since you can only use one of these aquisition modes, it makes sense to
allow only one application to open the device at a time.

Since the channels are using the same pacer, the sampling frequency
can not vary over the channels. Therefor it makes no sense to identify
every channel with a special device file. I'm only using /dev/adc00.

Hardware burst mode is used in all open() modes.
  The 12 bit boards sample in about  3 microsecs * num_channels.
  The 16 bit boards sample in about 10 microsecs * num_channels.

The data aquisition can be done in four steps:

Loading the module

  The module may be loaded by using insmod from root, for example.
      /sbin/insmod <path>/das1400.o

  The module may be setup for autoload.
      cp the das1400.o file to /lib/modules/preferred/misc
      add to file /etc/modules.conf the line
        "alias char-major-31 das1400" (assuming that /dev/adc00 uses major 31)
      if /etc/modules.conf dosn't exist make it with an editor as..
        "keep"
        "alias char-major-31 das1400"
      now the module will be autoloaded by open.

Setting up the hardware

  First open the device with one of the three hardware specific functions
    to set up the hardware for your needs. This open takes parameters of
    Mode, Sampling Frequency, Chans, the DMA-length and the Gain (Range).

    Mode is (Pacer, Software-trigger, and External-trigger).
    Sampling frequency is in Hertz.
    Chans N means sample channels 0..N
    DMA-length is in bytes and is used to tune the interrupting rate.
    Gain (Range) is described in the following table:

                     Bipolar                       Unipolar
          ------------------------------   --------------------------
               1401            1402           1401          1402
   Gain   --------------  --------------   ------------  ------------
      0   -10.0 .. +10.0  -10.0 .. +10.0   0.0 .. +10.0  0.0 .. +10.0
      1   -1.0  .. +1.0   -5.0  .. +5.0    0.0 .. +1.0   0.0 .. +5.0
      2   -0.1  .. +0.1   -2.5  .. +2.5    0.0 .. +0.1   0.0 .. +2.5
      3   -0.01 .. +0.01  -1.25 .. +1.25   0.0 .. +0.01  0.0 .. +1.25
    

  functions adcopen_1401_12, adcopen_1402_12 and adcopen_1402_16 are supplied
    which take the necessary parameters and open the device.
    These support the
      DAS-1401/12 (12 bit)
      DAS-1402/12 (12 bit)
      DAS-1402/16 (16 bit) board types.

Reading the data

  In Pacer mode, starting the pacer will clear the buffer and start
    conversion of the signals.  Use read(n) to get a buffer of data
    consisting of n datasets. A dataset is one sample from each channel.
    The buffer size is at least (n * # chans * 2) bytes.

  In soft mode, each read(n) will start a set of n channel measurements
    and wait for completion, returning the n datasets.

  In extern mode, the read will wait for the interrupt which results from
    the external trigger, sleeping the process. This mode is not completely
    coded and has not been tested.

Stopping the pacer

  After a while of data aquisition you may stop the pacer.

Digital I/O

  This board set has a minimal 4 bit digital capability.
  You can read or write a byte and the lower 4 bits are input/output
  on the connector pins.

Test

  You may test the driver and the hardware by the C program adcsample.
  The sampling rate may be observed using the C program adctime.
  The Ada support may be tested by the Ada programs adctest and adcpulse.

  Hint: Use the two jumpers provided with the board to jumper connector pin
  19 to 37 and 8 to 36.  This puts ground on channel 0 and the PC +5 volt
  supply on channel 1.  Using chans = 2 this gives two known values to measure.  

Library (libadc.a)

  The library includes the following functions:

  adcopen_1401_12 Open for the DAS-1401/12 (12 bit) board.
  adcopen_1402_12 Open for the DAS-1402/12 (12 bit) board.
  adcopen_1402_16 Open for the DAS-1402/16 (16 bit) board.
  adcread         Read the next group of datasets.
  DIOread         read 4 bits from connector pins 25,6,24,5.
                  Caution, these pins have multiple functions.
  DIOwrite        write 4 bits to connector pins 23,4,22,3.
  adclose         close
  ConvertData     For 12 bit boards, extracts 4 bit chan num and 12 bit value
                    from 16 bit board return value, and returns both.
                  For 16 bit board, returns chan num as 
                    sample number modulo num chans
  RawToReal       Converts int value to equivalent float value.

  adclib.h describes the library for C use.
  adc_lib.ads describes the library for Ada use.

Ada support
  adc_lib.ads     Ada specification file (like .h file)
  adctest.adb     Ada main for cursory test of Ada functionality.
  The gnat Ada compiler is obviously required.