A D A P T E C                                     A D A P T E C


          DATE:     December 2, 1989

          TO:       Dal Allan

          FROM:     Tom Newman (Adaptec, Inc)

          SUBJECT:  ATA PDIAG and DASP Timing

         ----------------------------------------------------------------------



          This document describes the following timing conditions to be
          included in the ATA specification:

          o  Power-on Reset
               -  One drive
               -  Two drives

          o  Soft Reset
               - One drive
               - Two drives

          o  Diagnostic Command
               - One drive
               - Two drives
               - Two drives -- drive 1 failed


          The timings assume the following:
          o    DASP- is driven by Drive 1 and received by Drive 0 at Power-on
               Reset time to indicate the present of Drive 1.  At all other
               times it is driven by Drive 0 and Drive 1 as the LED BUSY
               indicator.

          o    PDIAG- is driven by Drive 1 and received by Drive 0.  It is
               used by Drive 1 to tell Drive 0 that it has passed diagnostics
               and is ready to accept commands from the Host (BUSY bit is
               cleared).  This does not indicate that the drive is Ready,
               only that it can accept commands.  This line may remain
               asserted until the next Reset or Diagnostic command is
               received.

          o    Unless  indicated otherwise,  all  times are  relative  to the
               event  that   trigger  the  operation   (RESET-,  Soft  Reset,
               Diagnostic Command written).


          POWER-ON RESET -- ONE DRIVE          POWER-ON RESET -- ONE DRIVE

          --   RESET- asserted for a minimum of 300 nsecs.
          --   Drive 0 sets BUSY within 400 nsecs. after RESET- is negated.
          --   DASP- negated within 1 msec. after RESET- negated.
          --   Perform hardware initialization



                                           1





          --   Reverts to default condition
          --   Drive 0 waits 1 msec. then samples 500 msecs. for DASP-
               asserted from Drive 1.
          --   Drive 0 clears BUSY when ready to accept commands (within 31
               seconds).


          POWER-ON RESET -- TWO DRIVES          POWER-ON RESET -- TWO DRIVES

          --   RESET- asserted for a minimum of 300 nsecs.
          --   Drive 0 and Drive 1 set BUSY within 400 nsecs. after RESET-
               negated.
          --   DASP- negated within 1 msec. after RESET- negated.

          -DRIVE 1

          --   Negate PDIAG- before DASP- is asserted.
          --   Assert DASP- within 500 msecs after RESET- (shows Drive 1
               present).
          --   Perform hardware initialization/internal diagnostics.
          --   Revert to default condition
          --   Post diagnostic results to the ERROR register
          --   Clear BUSY when ready to accept commands.
          --   Assert PDIAG- to show ready to accept commands (within 30
               seconds from RESET-).
          --   Negate DASP- after the first command is received for Drive 1.
               DASP- is also negated if no command is received for Drive 1
               within 30 seconds after RESET-.

          --DRIVE 0

          --   Perform hardware initialization/internal diagnostics.
          --   Revert to default condition
          --   Post diagnostic results to the ERROR register
          --   After 1 msec., wait 500 msecs. for DASP- to be asserted (from
               Drive 1).
               If DASP- is not asserted, no Drive 1 present (see POWER-ON
               RESET -- ONE DRIVE operation).
          --   Wait up to 31 seconds for Drive 1 to assert PDIAG-,
               If PDIAG- is not asserted, set bit 7 in ERROR register.
          --   Clear BUSY when ready to accept commands (within 31 seconds).


          SOFT RESET -- ONE DRIVE          SOFT RESET -- ONE DRIVE

          --   Soft Reset (register 3F6) set by Host.
          --   Wait for Soft Reset cleared by Host.
          --   Drive 0 sets BUSY within 400 nsecs. after Soft Reset is
               cleared.
          --   Perform hardware initialization/internal diagnostics.
          --   Revert to default condition
          --   Post diagnostic results to the ERROR register
          --   Drive 0 clears BUSY when ready to accept commands (within 31
               seconds).


          SOFT RESET -- TWO DRIVES          SOFT RESET -- TWO DRIVES



                                           2






          --   Soft Reset (register 3F6) set by Host.
          --   Wait for Soft Reset cleared by Host.
          --   Drive 0 and Drive 1 set BUSY within 400 nsecs. after Soft
               Reset is cleared.
          --   Perform hardware initialization
          --   Revert to default condition

          -DRIVE 1

          --   Clear BUSY when ready to accept commands.
          --   Negate PDIAG- to show ready to accept commands (within 30
               seconds).

          --DRIVE 0

          --   Wait up to 31 seconds for Drive 1 to assert PDIAG-.
          --   Clear BUSY when ready to accept commands (within 31 seconds).


          DIAGNOSTIC COMMAND  -- ONE DRIVE (Passed)          DIAGNOSTIC COMMAND  -- ONE DRIVE (Passed)

          --   Drive 0 sets BUSY within 400 nsecs. after Diagnostic command
               received.
          --   Perform hardware initialization and internal diagnostics.
          --   Reset Command Block registers to default condition.
          --   Post diagnostic results to the ERROR register
          --   Drive 0 clears BUSY when ready to accept commands (within 31
               seconds).


          DIAGNOSTIC COMMAND -- TWO DRIVES (Passed)          DIAGNOSTIC COMMAND -- TWO DRIVES (Passed)

          --   Drive 0 and Drive 1 set BUSY within 400 nsecs. after
               Diagnostic command received.

          --DRIVE 1

          --   Negate PDIAG- within 1 msec. after command received.
          --   Perform hardware initialization and internal diagnostics.
          --   Reset Command Block registers to default condition.
          --   Post diagnostic results to the ERROR register
          --   Clear BUSY when ready to accept commands.
          --   Negate PDIAG- to show ready to accept commands (within 5
               seconds).

          --DRIVE 0

          --   Perform hardware initialization and internal diagnostics.
          --   Reset Command Block registers to default condition.
          --   Wait up to 6 seconds for Drive 1 to assert PDIAG-.
          --   Post diagnostic results to the ERROR register
          --   Clear BUSY when ready to accept commands (within 6 seconds).


          DIAGNOSTIC COMMAND  -- ONE DRIVE (Failed)          DIAGNOSTIC COMMAND  -- ONE DRIVE (Failed)




                                           3





          --   Drive 0 sets BUSY within 400 nsecs. after Diagnostic command
               received.
          --   Perform hardware initialization and internal diagnostics.
          --   Reset Command Block registers to default condition.
          --   Post diagnostic error to the ERROR register (failed)
          --   Drive 0 clears BUSY when ready to accept commands (within 6
               seconds)


          DIAGNOSTIC COMMAND -- TWO DRIVES (Drive 1 Failed)          DIAGNOSTIC COMMAND -- TWO DRIVES (Drive 1 Failed)

          --   Drive 0 and Drive 1 set BUSY within 400 nsecs. after
               Diagnostic command received.

          -DRIVE 1

          --   Negate PDIAG- within 1 msec. after command received.
          --   Perform hardware initialization and internal diagnostics.
          --   Reset Command Block registers to default condition.
          --   Post diagnostic error to the ERROR register
          --   Clear BUSY.
          --   PDIAG- is not negated indicating Drive 1 failed.

          --DRIVE 0

          --   Perform hardware initialization and internal diagnostics.
          --   Reset Command Block registers to default condition.
          --   Wait 6 seconds for Drive 1 to assert PDIAG- (PDIAG- is not
               asserted).
          --   Post diagnostic results to the ERROR register (bit 7 is set
               showing that Drive 1 failed diagnostics).
          --   Clear BUSY when ready to accept commands (within 6 seconds).




























                                           4